Gravitational Potential Energy
- Gravitational Potential Energy (GPE) of an object in a gravitational field is the object’s mass multiplied by the Potential at that point
- E_p = m V (where m is the mass of the object and V is the potential)
- E_p = { -G M m } over r (where M is the mass of the planet, m is the mass of the object and r is the distance from centre of planet)
- To calculate the change in potential energy for a mass moving between places, multiply the mass of the object by the change in potential
- Change of E_p = %DELTA E = m cdot %DELTA V = m( V_1 - V_2 )
- A spacecraft passing by a planet can exchange momentum with the planet; This saves fuel.
- So most spacecrafts going to other planets loop round various other planets on the way to increase their velocity.
- The Voyager missions in the 1970s used the rare line up of all planets to get to edge of solar system and are now heading out into interstellar space at a fast speed.
- To find the speed needed to escape a planet (escape velocity), put the two energies equal to each other E_K = E_p ~ -> ~ { 1 over 2 } m v^2 = { G M m } over r ~ -> ~ v_e = sqrt{ { 2 G M } over r} where v ~ > ~ v_e
- E_t = E_K + E_p where E_t is the total energy of a spacecraft. The total energy will always stay the same – if E_K halves then E_p will double.