PAG 10.2 – Observing forced oscillations
- Aim:
  - To observe forced oscillations
- Equipment:
  - Bare hacksaw blade
  - Heavy base clamp
  - Small piece of wood
  - Clamp stand
  - Vibration generator
  - Signal generator
  - 1 m ruler
  - Short piece of wire
  - 2 leads
- Steps:
  - Put the bare hacksaw blade in the base clamp
  - Estimate its natural frequency
  - Place the vibration generator on its side so it will oscillate horizontally
  - Connect it to the 6 ohm connections on the signal generator
  - Slip one end of the wire through the nut on the vibration generator and twist it to secure it and wrap the other end around the hacksaw blade
  - Fix the ruler horizontally level with the top of the hacksaw blade and take note of its mark on the ruler when at rest
  - Set the frequency on 1 Hz and measure then record the amplitude
  - Increase frequency by 1 Hz and measure then record the amplitude
  - Repeat step 8 till you reach 10 Hz
  - Increase frequency by 5 Hz and measure then record the amplitude
  - Repeat step 10 till you reach 50 Hz
  - Plot a graph of Frequency in Hz (x-axis) against amplitude in cm (y-axis)